## Slide 1: Cache
Compiled by:
Sarosh shahid

## Slide 2: Cache Miss
Find data in cache
MOV AL, [08]
00 | 47
01 | 25
02 | 5
03 | 6
04 | 88
05 | 99
06 | 21
07 | 58
08 | 57
09 | 98
0A | 65
0B | 22
Processor
Cache
Not Found
Memory
CACHE MISS
Place 57 in
cache
57
57
Find data in memory

## Slide 3: Cache Hit
Find data in cache
MOV AL, [08]
00 | 47
01 | 25
02 | 5
03 | 6
04 | 88
05 | 99
06 | 21
07 | 58
08 | 57
09 | 98
0A | 65
0B | 22
Processor
Cache
Found
Memory
CACHE HIT
Data 57 in
cache
57

## Slide 4: Cache Miss
MOV AL, [08]
00 | 47
01 | 25
02 | 5
03 | 6
04 | 88
05 | 99
06 | 21
07 | 58
08 | 57
09 | 98
0A | 65
0B | 22
Processor
L1 Cache
Memory
L2 Cache
Find data in
L1 cache
Not Found
L1 CACHE MISS
Find data in
L2 cache
Not Found
Find data in
memory
L2 CACHE MISS
57
57
57
Place 57 in
L2 cache
Place 57 in
L1 cache

## Slide 5: Cache Miss
MOV AL, [08]
00 | 47
01 | 25
02 | 5
03 | 6
04 | 88
05 | 99
06 | 21
07 | 58
08 | 57
09 | 98
0A | 65
0B | 22
Processor
L1 Cache
Memory
L2 Cache
Find data in
L1 cache
Not Found
L1 CACHE MISS
Find data in
L2 cache
Found
L2 CACHE HIT
57
57
Data 57 in
L2 cache
Place 57 in
L1 cache

## Slide 6: Locality
Temporal Locality:
  Locality in time
  If data used recently, likely to use it again soon
  How to exploit: keep recently accessed data in higher levels of memory hierarchy
Spatial Locality:
  Locality in space
  If data used recently, likely to use nearby data soon
  How to exploit: when access data, bring nearby data into higher levels of memory hierarchy too

## Slide 7: Locality
Temporal Locality:
    If data used recently, likely to use it again soon “Variables i and a”
Spatial Locality:
    If data used recently, likely to use nearby data soon “Array A”

## Slide 8: What data is held in cache?
Ideally, cache anticipates needed data and puts it in cache
But impossible to predict future
Use past to predict future – temporal and spatial locality:
  Temporal locality: copy newly accessed data into cache
  Spatial locality: copy neighboring data into cache too

## Slide 9: Cache Performance Analysis

## Slide 10: Cache Performance Analysis
Example
Suppose a program has 2000 data access instructions (load or stores), and 1250 of these requested data values are found in the cache. The other 750 data values are supplied to the processor by main memory or disk memory. What are the miss and hit rates for the cache?
Solution

## Slide 11: Cache Terminologies
Cache Capacity C = Total number of bytes that can be stored in the cache
Data is transferred between memory and cache in blocks of fixed size called cache lines or cache blocks.
b = Block size
Block 0 | 
Block 1 | 
Block 2 | 
Block 3 | 
Block 4 | 
Block 5 | 
Block 6 | 
Block 7 | 
Cache
Cache Line

## Slide 12: Cache Terminologies
Block 0 = 4B |  |  |  | 
Block 1 = 4B |  |  |  | 
b = 32 bits = 4B
C = 64 bits = 8B
Cache
Cache Line

## Slide 13: Block Size
Block 0 | 00 | 47
 | 01 | 25
 | 02 | 5
 | 03 | 6
Block 1 | 04 | 88
 | 05 | 99
 | 06 | 21
 | 07 | 58
Block 2 | 08 | 57
 | 09 | 98
 | 0A | 65
 | 0B | 22
Block 3 | 0C | 66
 | 0D | 8
 | 0E | 55
 | 0F | 1
Memory
Block 0 = 4B |  |  |  | 
Block 1 = 4B |  |  |  | 
b = 32 bits = 4B
C = 64 bits = 8B
Cache
Cache Line
One block of cache can hold 4Bytes so memory is also logically
divided into equal chunks of 4 bytes and all 4 bytes are brought in the cache at once.

## Slide 14: Block Size
Block 0 = 4B | 57 | 98 | 65 | 22
Block 1 = 4B |  |  |  | 
b = 32 bits = 4B
C = 64 bits = 8B
Cache
Cache Line
Block 0 | 00 | 47
 | 01 | 25
 | 02 | 5
 | 03 | 6
Block 1 | 04 | 88
 | 05 | 99
 | 06 | 21
 | 07 | 58
Block 2 | 08 | 57
 | 09 | 98
 | 0A | 65
 | 0B | 22
Block 3 | 0C | 66
 | 0D | 8
 | 0E | 55
 | 0F | 1
MOV AL, [09]
Instead of bringing only [09] will bring the whole block in the cache
Block size = 4B so will bring 4Bytes and as the address [09] is in “Block 2” and it maps to the “yellow colored” block of the cache… (Spatial Locality)

## Slide 15: Offset Bits
Offset | 00 | 01 | 10 | 11
Block 0 = 4B | 57 | 98 | 65 | 22
Block 1 = 4B |  |  |  | 
B = 32 bits = 4B
C = 64 bits = 8B
Cache
Cache Line
Block 0 | 00 | 47
 | 01 | 25
 | 02 | 5
 | 03 | 6
Block 1 | 04 | 88
 | 05 | 99
 | 06 | 21
 | 07 | 58
Block 2 | 08 | 57
 | 09 | 98
 | 0A | 65
 | 0B | 22
Block 3 | 0C | 66
 | 0D | 8
 | 0E | 55
 | 0F | 1
MOV AL, [09]
Offset bits are used to identify the data
[09] is at offset “01b or 1”
[0A] is at offset “10b or 2” and so on

## Slide 16: Cache Terminology
Capacity (C):
  number of data bytes in cache
Block size (b):
  bytes of data brought into cache at once
Number of blocks (B = C/b):
  number of blocks in cache: B = C/b
Degree of associativity (N):
  number of blocks in a set
Number of sets (S = B/N):
  each memory address maps to exactly one cache set

## Slide 17: Cache Types
Set # 0 | 
Set # 1 | 
Set # 2 | 
Set # 3 | 
Set # 4 | 
Set # 5 | 
Set # 6 | 
Set # 7 | 
Set # 0 | 
Set # 1 | 
Set # 2 | 
Set # 3 | 
Set # 0 | 
Set # 0 | 
Set # 1 | 
Direct Mapped Cache
N-way Associative Cache
Fully Associative Cache
Four-way Associative Cache
Two-way Associative Cache
One-way Associative Cache
1 block per set
N blocks per set
All cache blocks in one set

## Slide 18: Design Cache
b = 4B
C = 64B
N = 1 (Direct Mapped)
  B = C/b = 16
S = B/N = 16/1 = 16
Offset Sets | 00 | 01 | 10 | 11
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
…….. |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 

## Slide 19: Design Cache
b = 32B
C = 128B
N = 1 (Direct Mapped)
  B = C/b = 128/32 =4
S = B/N = 4/1 = 4
Offset Sets | 00000 | 00001 | 00010 | ….. | 11110 | 11111
00 |  |  |  |  |  | 
01 |  |  |  |  |  | 
10 |  |  |  |  |  | 
11 |  |  |  |  |  | 

## Slide 20: Design Cache
b = 4B
C = 32B
N = 4 (4-way associative)
  B = C/b = 32/4 =8
S = B/N = 8/4 = 2
Offset Sets | 00 | 01 | 10 | 11
0 |  |  |  | 
1 |  |  |  | 

## Slide 21: Design Cache
b = 8B
Full Associative Cache
Single set with 4-ways
  C = 8B * 4 (ways) = 32B
  B = C/b = 32/8 = 4
S = B/N = 4/4 = 1
Offset Sets | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
0 |  |  |  |  |  |  |  | 

## Slide 22: Cache Terminologies
Tag Bits - A unique identifier for a group of data. Because different regions of memory may be mapped into a single block, the tag is used to differentiate between them.
We need to add tags to the cache, which supply the rest of the address bits to let us distinguish between different memory locations that map to the same cache block.
Valid bit (V)- A bit of information that indicates whether the data in a block is valid (1) or not (0).
  At the very start, the cache is empty and does not contain valid data.
  We should account for this by adding a valid bit for each cache block.
  When the system is initialized, all the valid bits are set to 0. When data is loaded into a particular cache block, the corresponding valid bit is set to 1.

## Slide 23: Example 01
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 0 |  |  |  |  | 
101 | 0 |  |  |  |  | 
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Convert to
binary
b = 4B
C = 32B
N = 1 (Direct Mapped)
Addresses are 12 bits
  B = C/b = 8
S = B/N = 8/1 = 8
Processor Memory Access Sequence
0x014
0xFF0
0x0F7
0xC03
0x0F3
000 | 00000000
004 | 00000004
008 | 00000008
00C | 0000000C
010 | 00000010
014 | 00000014
018 | 00000018
01C | 0000001C
020 | 00000020
……. | 
FF4 | 00000FF4
FF8 | 00000FF8
FFC | 00000FFC
Memory
Cache
0x014
0000 0001 0100
Tag Bits Set bits Offset bits
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 0 |  |  |  |  | 
101 | 1 | 0000000 | 00 | 00 | 00 | 14
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
1
Cache Miss = 1 Cache Hit = 0

## Slide 24: Example 01
Convert to
binary
b = 4B
C = 32B
N = 1 (Direct Mapped)
Addresses are 12 bits
  B = C/b = 8
S = B/N = 8/1 = 8
Processor Memory Access Sequence
0x014
0xFF0
0x0F7
0xC03
0x0F3
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 1111111 | 00 | 00 | 0F | F0
101 | 1 | 0000000 | 00 | 00 | 00 | 14
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
000 | 00000000
004 | 00000004
008 | 00000008
00C | 0000000C
010 | 00000010
014 | 00000014
018 | 00000018
01C | 0000001C
020 | 00000020
……. | 
FF4 | 00000FF4
FF8 | 00000FF8
FFC | 00000FFC
Memory
Cache
0xFF0
1111 1111 0000
Tag Bits Set bits Offset bits
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 1111111 |  |  |  | 
101 | 1 | 0000000 | 00 | 00 | 00 | 14
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Cache Miss = 2 Cache Hit = 0

## Slide 25: Example 01
Convert to
binary
b = 4B
C = 32B
N = 1 (Direct Mapped)
Addresses are 12 bits
  B = C/b = 8
S = B/N = 8/1 = 8
Processor Memory Access Sequence
0x014
0xFF0
0x0F7
0xC03
0x0F3
000 | 00000000
004 | 00000004
008 | 00000008
00C | 0000000C
010 | 00000010
014 | 00000014
018 | 00000018
01C | 0000001C
020 | 00000020
……. | 
FF4 | 00000FF4
FF8 | 00000FF8
FFC | 00000FFC
Memory
Cache
0x0F7
0000 1111 0111
Tag Bits Set bits Offset bits
Data already present in the set “101”. To check whether it’s the same data we need “compare the tag bits”. As
0000000 ≠ 0000111 It means we have to replace the data.
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 1111111 | 00 | 00 | 0F | F0
101 | 1 | 0000000 | 00 | 00 | 00 | 14
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 1111111 | 00 | 00 | 0F | F0
101 | 1 | 0000111 | 00 | 00 | 00 | 14
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Cache Miss = 3 Cache Hit = 0

## Slide 26: Example 01
Convert to
binary
b = 4B
C = 32B
N = 1 (Direct Mapped)
Addresses are 12 bits
  B = C/b = 8
S = B/N = 8/1 = 8
Processor Memory Access Sequence
0x014
0xFF0
0x0F7
0xC03
0x0F3
000 | 00000000
004 | 00000004
008 | 00000008
00C | 0000000C
010 | 00000010
014 | 00000014
018 | 00000018
01C | 0000001C
020 | 00000020
……. | 
FF4 | 00000FF4
FF8 | 00000FF8
FFC | 00000FFC
Memory
Cache
0xC03
1100 0000 0011
Tag Bits Set bits Offset bits
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 1111111 | 00 | 00 | 0F | F0
101 | 1 | 0000111 | 00 | 00 | 00 | F7
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 1 | 1100000 | 00 | 00 | 0C | 03
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 1111111 | 00 | 00 | 0F | F0
101 | 1 | 0000111 | 00 | 00 | 00 | F7
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Cache Miss = 4 Cache Hit = 0

## Slide 27: Example 01
Convert to
binary
b = 4B
C = 32B
N = 1 (Direct Mapped)
Addresses are 12 bits
  B = C/b = 8
S = B/N = 8/1 = 8
Processor Memory Access Sequence
0x014
0xFF0
0x0F7
0xC03
0x0F3
000 | 00000000
004 | 00000004
008 | 00000008
00C | 0000000C
010 | 00000010
014 | 00000014
018 | 00000018
01C | 0000001C
020 | 00000020
……. | 
FF4 | 00000FF4
FF8 | 00000FF8
FFC | 00000FFC
Memory
Cache
0x0F3
0000 1111 0011
Tag Bits Set bits Offset bits
Data already present in the set “101”. To check whether it’s the same data we need “compare the tag bits”. As
0000111 = 0000111 It means we found the data and it’s a CACHE HIT.
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 1 | 1100000 | 00 | 00 | 0C | 03
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 0000111 | 00 | 00 | 00 | F7
101 | 1 | 0000000 | 00 | 00 | 00 | 14
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Cache Miss = 4 Cache Hit = 1