## Slide 1
CACHE Examples

## Slide 2: Example 01
Consider a 2-way associative cache where
b = 4 bytes
C = 16bytes
Memory address bits = 8 bits
The memory access sequence and memory is provided. Find the cache miss and hit rate. For write hits and misses use write back and write allocate policies respectively.

## Slide 3: Example 01
Address (dec) | Data (Hex)
8 | aa aa aa aa
12 | bb bb bb bb
16 | cc cc cc cc
20 | dd dd dd dd
24 | ab ab ab ab
28 | ff ff ff ff
32 | 84 84 84 84
36 | 12 34 56 78
40 | 87 65 43 21
44 | 09 09 90 90
48 | ee ee ee ee
52 | 97 85 64 87
56 | 1b 1b 1b 1b
60 | 00 00 00 00
64 | 0f 0f 0f 0f
Set bits | Tag bits | V bit | LRU bit | Dirty bit | Data |  |  | 
 |  |  |  |  | 00 | 01 | 10 | 11
0 |  | 0 |  | 0 |  |  |  | 
 |  | 0 |  | 0 |  |  |  | 
1 |  | 0 |  | 0 |  |  |  | 
 |  | 0 |  | 0 |  |  |  | 
Cache Miss = 0 Cache Hit = 0
Op | Address(dec) | Data (Hex)
LD | 28 | 
LD | 44 | 
ST | 52 | 01 01 01 01
ST | 44 | 02 02 02 02
LD | 24 | 
ST | 60 | dd dd dd dd
ST | 64 | e0 e0 0e 0e
LD | 20 | 
ST | 16 | 11 11 11 11

## Slide 4: Example 01
Address (dec) | Data (Hex)
8 | aa aa aa aa
12 | bb bb bb bb
16 | cc cc cc cc
20 | dd dd dd dd
24 | ab ab ab ab
28 | ff ff ff ff
32 | 84 84 84 84
36 | 12 34 56 78
40 | 87 65 43 21
44 | 09 09 90 90
48 | ee ee ee ee
52 | 97 85 64 87
56 | 1b 1b 1b 1b
60 | 00 00 00 00
64 | 0f 0f 0f 0f
Set bits | Tag bits | V bit | LRU bit | Dirty bit | Data |  |  | 
 |  |  |  |  | 00 | 01 | 10 | 11
0 |  | 0 |  | 0 |  |  |  | 
 |  | 0 |  | 0 |  |  |  | 
1 | 00011 | 1 | 0 | 0 | ff | ff | ff | ff
 |  | 0 |  | 0 |  |  |  | 
Convert to
binary
28
0001 1100
Tag Bits Set bits Offset bits
Cache Miss = 1 Cache Hit = 0
Op | Address(dec) | Data (Hex)
LD | 28 | 
LD | 44 | 
ST | 52 | 01 01 01 01
ST | 44 | 02 02 02 02
LD | 24 | 
ST | 60 | dd dd dd dd
ST | 64 | e0 e0 0e 0e
LD | 20 | 
ST | 16 | 11 11 11 11

## Slide 5: Example 01
Address (dec) | Data (Hex)
8 | aa aa aa aa
12 | bb bb bb bb
16 | cc cc cc cc
20 | dd dd dd dd
24 | ab ab ab ab
28 | ff ff ff ff
32 | 84 84 84 84
36 | 12 34 56 78
40 | 87 65 43 21
44 | 09 09 90 90
48 | ee ee ee ee
52 | 97 85 64 87
56 | 1b 1b 1b 1b
60 | 00 00 00 00
64 | 0f 0f 0f 0f
Set bits | Tag bits | V bit | LRU bit | Dirty bit | Data |  |  | 
 |  |  |  |  | 00 | 01 | 10 | 11
0 |  | 0 |  | 0 |  |  |  | 
 |  | 0 |  | 0 |  |  |  | 
1 | 00011 | 1 | 1 | 0 | ff | ff | ff | ff
 | 00101 | 1 | 0 | 0 | 09 | 09 | 90 | 90
Convert to
binary
44
0010 1100
Tag Bits Set bits Offset bits
Cache Miss = 2 Cache Hit = 0
Op | Address(dec) | Data (Hex)
LD | 28 | 
LD | 44 | 
ST | 52 | 01 01 01 01
ST | 44 | 02 02 02 02
LD | 24 | 
ST | 60 | dd dd dd dd
ST | 64 | e0 e0 0e 0e
LD | 20 | 
ST | 16 | 11 11 11 11

## Slide 6: Example 01
Address (dec) | Data (Hex)
8 | aa aa aa aa
12 | bb bb bb bb
16 | cc cc cc cc
20 | dd dd dd dd
24 | ab ab ab ab
28 | ff ff ff ff
32 | 84 84 84 84
36 | 12 34 56 78
40 | 87 65 43 21
44 | 09 09 90 90
48 | ee ee ee ee
52 | 01 01 01 01
56 | 1b 1b 1b 1b
60 | 00 00 00 00
64 | 0f 0f 0f 0f
Set bits | Tag bits | V bit | LRU bit | Dirty bit | Data |  |  | 
 |  |  |  |  | 00 | 01 | 10 | 11
0 |  | 0 |  | 0 |  |  |  | 
 |  | 0 |  | 0 |  |  |  | 
1 | 00110 | 1 | 0 | 0 | 01 | 01 | 01 | 01
 | 00101 | 1 | 1 | 0 | 09 | 09 | 90 | 90
Convert to
binary
52
0011 0100
Tag Bits Set bits Offset bits
Cache Miss = 3 Cache Hit = 0
Op | Address(dec) | Data (Hex)
LD | 28 | 
LD | 44 | 
ST | 52 | 01 01 01 01
ST | 44 | 02 02 02 02
LD | 24 | 
ST | 60 | dd dd dd dd
ST | 64 | e0 e0 0e 0e
LD | 20 | 
ST | 16 | 11 11 11 11

## Slide 7: Example 01
Address (dec) | Data (Hex)
8 | aa aa aa aa
12 | bb bb bb bb
16 | cc cc cc cc
20 | dd dd dd dd
24 | ab ab ab ab
28 | ff ff ff ff
32 | 84 84 84 84
36 | 12 34 56 78
40 | 87 65 43 21
44 | 09 09 90 90
48 | ee ee ee ee
52 | 01 01 01 01
56 | 1b 1b 1b 1b
60 | 00 00 00 00
64 | 0f 0f 0f 0f
Set bits | Tag bits | V bit | LRU bit | Dirty bit | Data |  |  | 
 |  |  |  |  | 00 | 01 | 10 | 11
0 |  | 0 |  | 0 |  |  |  | 
 |  | 0 |  | 0 |  |  |  | 
1 | 00110 | 1 | 1 | 0 | 01 | 01 | 01 | 01
 | 00101 | 1 | 0 | 1 | 02 | 02 | 02 | 02
Convert to
binary
44
0010 1100
Tag Bits Set bits Offset bits
Cache Miss = 3 Cache Hit = 1
Op | Address(dec) | Data (Hex)
LD | 28 | 
LD | 44 | 
ST | 52 | 01 01 01 01
ST | 44 | 02 02 02 02
LD | 24 | 
ST | 60 | dd dd dd dd
ST | 64 | e0 e0 0e 0e
LD | 20 | 
ST | 16 | 11 11 11 11

## Slide 8: Example 01
Set bits | Tag bits | V bit | LRU bit | Dirty bit | Data |  |  | 
 |  |  |  |  | 00 | 01 | 10 | 11
0 | 00011 | 1 | 0 | 0 | ab | ab | ab | ab
 |  | 0 |  | 0 |  |  |  | 
1 | 00110 | 1 | 1 | 0 | 01 | 01 | 01 | 01
 | 00101 | 1 | 0 | 1 | 02 | 02 | 02 | 02
Convert to
binary
24
0001 1000
Tag Bits Set bits Offset bits
Cache Miss = 4 Cache Hit = 1
Op | Address(dec) | Data (Hex)
LD | 28 | 
LD | 44 | 
ST | 52 | 01 01 01 01
ST | 44 | 02 02 02 02
LD | 24 | 
ST | 60 | dd dd dd dd
ST | 64 | e0 e0 0e 0e
LD | 20 | 
ST | 16 | 11 11 11 11
Address (dec) | Data (Hex)
8 | aa aa aa aa
12 | bb bb bb bb
16 | cc cc cc cc
20 | dd dd dd dd
24 | ab ab ab ab
28 | ff ff ff ff
32 | 84 84 84 84
36 | 12 34 56 78
40 | 87 65 43 21
44 | 09 09 90 90
48 | ee ee ee ee
52 | 01 01 01 01
56 | 1b 1b 1b 1b
60 | 00 00 00 00
64 | 0f 0f 0f 0f

## Slide 9: Example 01
Set bits | Tag bits | V bit | LRU bit | Dirty bit | Data |  |  | 
 |  |  |  |  | 00 | 01 | 10 | 11
0 | 00011 | 1 | 0 | 0 | ab | ab | ab | ab
 |  | 0 |  | 0 |  |  |  | 
1 | 00111 | 1 | 0 | 0 | dd | dd | dd | dd
 | 00101 | 1 | 1 | 1 | 02 | 02 | 02 | 02
Convert to
binary
60
0011 1100
Tag Bits Set bits Offset bits
Cache Miss = 5 Cache Hit = 1
Op | Address(dec) | Data (Hex)
LD | 28 | 
LD | 44 | 
ST | 52 | 01 01 01 01
ST | 44 | 02 02 02 02
LD | 24 | 
ST | 60 | dd dd dd dd
ST | 64 | e0 e0 0e 0e
LD | 20 | 
ST | 16 | 11 11 11 11
Address (dec) | Data (Hex)
8 | aa aa aa aa
12 | bb bb bb bb
16 | cc cc cc cc
20 | dd dd dd dd
24 | ab ab ab ab
28 | ff ff ff ff
32 | 84 84 84 84
36 | 12 34 56 78
40 | 87 65 43 21
44 | 09 09 90 90
48 | ee ee ee ee
52 | 01 01 01 01
56 | 1b 1b 1b 1b
60 | dd dd dd dd
64 | 0f 0f 0f 0f

## Slide 10: Example 01
Set bits | Tag bits | V bit | LRU bit | Dirty bit | Data |  |  | 
 |  |  |  |  | 00 | 01 | 10 | 11
0 | 00011 | 1 | 1 | 0 | ab | ab | ab | ab
 | 01000 | 1 | 0 | 0 | e0 | e0 | 0e | 0e
1 | 00111 | 1 | 0 | 0 | dd | dd | dd | dd
 | 00101 | 1 | 1 | 1 | 02 | 02 | 02 | 02
Convert to
binary
64
0100 0000
Tag Bits Set bits Offset bits
Cache Miss = 6 Cache Hit = 1
Op | Address(dec) | Data (Hex)
LD | 28 | 
LD | 44 | 
ST | 52 | 01 01 01 01
ST | 44 | 02 02 02 02
LD | 24 | 
ST | 60 | dd dd dd dd
ST | 64 | e0 e0 0e 0e
LD | 20 | 
ST | 16 | 11 11 11 11
Address (dec) | Data (Hex)
8 | aa aa aa aa
12 | bb bb bb bb
16 | cc cc cc cc
20 | dd dd dd dd
24 | ab ab ab ab
28 | ff ff ff ff
32 | 84 84 84 84
36 | 12 34 56 78
40 | 87 65 43 21
44 | 09 09 90 90
48 | ee ee ee ee
52 | 01 01 01 01
56 | 1b 1b 1b 1b
60 | dd dd dd dd
64 | e0 e0 0e 0e

## Slide 11: Example 01
Set bits | Tag bits | V bit | LRU bit | Dirty bit | Data |  |  | 
 |  |  |  |  | 00 | 01 | 10 | 11
0 | 00011 | 1 | 1 | 0 | ab | ab | ab | ab
 | 01000 | 1 | 0 | 0 | e0 | e0 | 0e | 0e
1 | 00111 | 1 | 1 | 0 | dd | dd | dd | dd
 | 00101 | 1 | 0 | 0 | dd | dd | dd | dd
Convert to
binary
20
0001 0100
Tag Bits Set bits Offset bits
Cache Miss = 7 Cache Hit = 1
Op | Address(dec) | Data (Hex)
LD | 28 | 
LD | 44 | 
ST | 52 | 01 01 01 01
ST | 44 | 02 02 02 02
LD | 24 | 
ST | 60 | dd dd dd dd
ST | 64 | e0 e0 0e 0e
LD | 20 | 
ST | 16 | 11 11 11 11
Address (dec) | Data (Hex)
8 | aa aa aa aa
12 | bb bb bb bb
16 | cc cc cc cc
20 | dd dd dd dd
24 | ab ab ab ab
28 | ff ff ff ff
32 | 84 84 84 84
36 | 12 34 56 78
40 | 87 65 43 21
44 | 02 02 02 02
48 | ee ee ee ee
52 | 01 01 01 01
56 | 1b 1b 1b 1b
60 | dd dd dd dd
64 | e0 e0 0e 0e

## Slide 12: Example 01
Set bits | Tag bits | V bit | LRU bit | Dirty bit | Data |  |  | 
 |  |  |  |  | 00 | 01 | 10 | 11
0 | 00010 | 1 | 0 | 0 | 11 | 11 | 11 | 11
 | 01000 | 1 | 1 | 0 | e0 | e0 | 0e | 0e
1 | 00111 | 1 | 1 | 0 | dd | dd | dd | dd
 | 00101 | 1 | 0 | 0 | dd | dd | dd | dd
Convert to
binary
16
0001 0000
Tag Bits Set bits Offset bits
Cache Miss = 8 Cache Hit = 1
Op | Address(dec) | Data (Hex)
LD | 28 | 
LD | 44 | 
ST | 52 | 01 01 01 01
ST | 44 | 02 02 02 02
LD | 24 | 
ST | 60 | dd dd dd dd
ST | 64 | e0 e0 0e 0e
LD | 20 | 
ST | 16 | 11 11 11 11
Address (dec) | Data (Hex)
8 | aa aa aa aa
12 | bb bb bb bb
16 | 11 11 11 11
20 | dd dd dd dd
24 | ab ab ab ab
28 | ff ff ff ff
32 | 84 84 84 84
36 | 12 34 56 78
40 | 87 65 43 21
44 | 02 02 02 02
48 | ee ee ee ee
52 | 01 01 01 01
56 | 1b 1b 1b 1b
60 | dd dd dd dd
64 | e0 e0 0e 0e

## Slide 13: Example 02
Consider a direct mapped cache where each block holds 4 bytes data and 4 sets. Consider write through and write no-allocate strategies on write hits and miss respectively. The memory addresses are 8-bits.

## Slide 14: Example 02
Op | Address(binary) | Data (dec)
LD | 00 01 11 00 | 
LD | 00 10 10 00 | 
ST | 00 10 01 00 | 32
LD | 00 01 00 00 | 
ST | 00 11 01 00 | 642
LD | 00 10 10 00 | 
LD | 00 01 11 00 | 
ST | 00 10 01 00 | 124
LD | 00 10 00 00 | 
LD | 00 10 10 00 | 
Address (binary) | Data (dec)
00 00 10 00 | 435
00 00 11 00 | 9
00 01 00 00 | 47
00 01 01 00 | 13
00 01 10 00 | 7586
00 01 11 00 | 86
00 10 00 00 | 43
00 10 01 00 | 48
00 10 10 00 | 673
00 10 11 00 | 4
00 11 00 00 | 972
00 11 01 00 | 1003
Sets | Tag | V bit | Data
00 |  | 0 | 
01 |  | 0 | 
10 |  | 0 | 
11 |  | 0 | 
Cache Miss = 0 Cache Hit = 0

## Slide 15: Example 02
Op | Address(binary) | Data (dec)
LD | 00 01 11 00 | 
LD | 00 10 10 00 | 
ST | 00 10 01 00 | 32
LD | 00 01 00 00 | 
ST | 00 11 01 00 | 642
LD | 00 10 10 00 | 
LD | 00 01 11 00 | 
ST | 00 10 01 00 | 124
LD | 00 10 00 00 | 
LD | 00 10 10 00 | 
Address (binary) | Data (dec)
00 00 10 00 | 435
00 00 11 00 | 9
00 01 00 00 | 47
00 01 01 00 | 13
00 01 10 00 | 7586
00 01 11 00 | 86
00 10 00 00 | 43
00 10 01 00 | 48
00 10 10 00 | 673
00 10 11 00 | 4
00 11 00 00 | 972
00 11 01 00 | 1003
Sets | Tag | V bit | Data
00 |  | 0 | 
01 |  | 0 | 
10 |  | 0 | 
11 | 0001 | 1 | 86
Cache Miss = 1 Cache Hit = 0

## Slide 16: Example 02
Op | Address(binary) | Data (dec)
LD | 00 01 11 00 | 
LD | 00 10 10 00 | 
ST | 00 10 01 00 | 32
LD | 00 01 00 00 | 
ST | 00 11 01 00 | 642
LD | 00 10 10 00 | 
LD | 00 01 11 00 | 
ST | 00 10 01 00 | 124
LD | 00 10 00 00 | 
LD | 00 10 10 00 | 
Address (binary) | Data (dec)
00 00 10 00 | 435
00 00 11 00 | 9
00 01 00 00 | 47
00 01 01 00 | 13
00 01 10 00 | 7586
00 01 11 00 | 86
00 10 00 00 | 43
00 10 01 00 | 48
00 10 10 00 | 673
00 10 11 00 | 4
00 11 00 00 | 972
00 11 01 00 | 1003
Sets | Tag | V bit | Data
00 |  | 0 | 
01 |  | 0 | 
10 | 0010 | 1 | 673
11 | 0001 | 1 | 86
Cache Miss = 2 Cache Hit = 0

## Slide 17: Example 02
Op | Address(binary) | Data (dec)
LD | 00 01 11 00 | 
LD | 00 10 10 00 | 
ST | 00 10 01 00 | 32
LD | 00 01 00 00 | 
ST | 00 11 01 00 | 642
LD | 00 10 10 00 | 
LD | 00 01 11 00 | 
ST | 00 10 01 00 | 124
LD | 00 10 00 00 | 
LD | 00 10 10 00 | 
Address (binary) | Data (dec)
00 00 10 00 | 435
00 00 11 00 | 9
00 01 00 00 | 47
00 01 01 00 | 13
00 01 10 00 | 7586
00 01 11 00 | 86
00 10 00 00 | 43
00 10 01 00 | 32
00 10 10 00 | 673
00 10 11 00 | 4
00 11 00 00 | 972
00 11 01 00 | 1003
Sets | Tag | V bit | Data
00 |  | 0 | 
01 |  | 0 | 
10 | 0010 | 1 | 673
11 | 0001 | 1 | 86
Cache Miss = 3 Cache Hit = 0

## Slide 18: Example 02
Op | Address(binary) | Data (dec)
LD | 00 01 11 00 | 
LD | 00 10 10 00 | 
ST | 00 10 01 00 | 32
LD | 00 01 00 00 | 
ST | 00 11 01 00 | 642
LD | 00 10 10 00 | 
LD | 00 01 11 00 | 
ST | 00 10 01 00 | 124
LD | 00 10 00 00 | 
LD | 00 10 10 00 | 
Address (binary) | Data (dec)
00 00 10 00 | 435
00 00 11 00 | 9
00 01 00 00 | 47
00 01 01 00 | 13
00 01 10 00 | 7586
00 01 11 00 | 86
00 10 00 00 | 43
00 10 01 00 | 32
00 10 10 00 | 673
00 10 11 00 | 4
00 11 00 00 | 972
00 11 01 00 | 1003
Sets | Tag | V bit | Data
00 | 0001 | 1 | 47
01 |  | 0 | 
10 | 0010 | 1 | 673
11 | 0001 | 1 | 86
Cache Miss = 4 Cache Hit = 0

## Slide 19: Example 02
Op | Address(binary) | Data (dec)
LD | 00 01 11 00 | 
LD | 00 10 10 00 | 
ST | 00 10 01 00 | 32
LD | 00 01 00 00 | 
ST | 00 11 01 00 | 642
LD | 00 10 10 00 | 
LD | 00 01 11 00 | 
ST | 00 10 01 00 | 124
LD | 00 10 00 00 | 
LD | 00 10 10 00 | 
Address (binary) | Data (dec)
00 00 10 00 | 435
00 00 11 00 | 9
00 01 00 00 | 47
00 01 01 00 | 13
00 01 10 00 | 7586
00 01 11 00 | 86
00 10 00 00 | 43
00 10 01 00 | 32
00 10 10 00 | 673
00 10 11 00 | 4
00 11 00 00 | 972
00 11 01 00 | 642
Sets | Tag | V bit | Data
00 | 0001 | 1 | 47
01 |  | 0 | 
10 | 0010 | 1 | 673
11 | 0001 | 1 | 86
Cache Miss = 5 Cache Hit = 0

## Slide 20: Example 02
Op | Address(binary) | Data (dec)
LD | 00 01 11 00 | 
LD | 00 10 10 00 | 
ST | 00 10 01 00 | 32
LD | 00 01 00 00 | 
ST | 00 11 01 00 | 642
LD | 00 10 10 00 | 
LD | 00 01 11 00 | 
ST | 00 10 01 00 | 124
LD | 00 10 00 00 | 
LD | 00 10 10 00 | 
Address (binary) | Data (dec)
00 00 10 00 | 435
00 00 11 00 | 9
00 01 00 00 | 47
00 01 01 00 | 13
00 01 10 00 | 7586
00 01 11 00 | 86
00 10 00 00 | 43
00 10 01 00 | 32
00 10 10 00 | 673
00 10 11 00 | 4
00 11 00 00 | 972
00 11 01 00 | 642
Sets | Tag | V bit | Data
00 | 0001 | 1 | 47
01 |  | 0 | 
10 | 0010 | 1 | 673
11 | 0001 | 1 | 86
Cache Miss = 5 Cache Hit = 1

## Slide 21: Example 02
Op | Address(binary) | Data (dec)
LD | 00 01 11 00 | 
LD | 00 10 10 00 | 
ST | 00 10 01 00 | 32
LD | 00 01 00 00 | 
ST | 00 11 01 00 | 642
LD | 00 10 10 00 | 
LD | 00 01 11 00 | 
ST | 00 10 01 00 | 124
LD | 00 10 00 00 | 
LD | 00 10 10 00 | 
Address (binary) | Data (dec)
00 00 10 00 | 435
00 00 11 00 | 9
00 01 00 00 | 47
00 01 01 00 | 13
00 01 10 00 | 7586
00 01 11 00 | 86
00 10 00 00 | 43
00 10 01 00 | 32
00 10 10 00 | 673
00 10 11 00 | 4
00 11 00 00 | 972
00 11 01 00 | 642
Sets | Tag | V bit | Data
00 | 0001 | 1 | 47
01 |  | 0 | 
10 | 0010 | 1 | 673
11 | 0001 | 1 | 86
Cache Miss = 5 Cache Hit = 2

## Slide 22: Example 02
Op | Address(binary) | Data (dec)
LD | 00 01 11 00 | 
LD | 00 10 10 00 | 
ST | 00 10 01 00 | 32
LD | 00 01 00 00 | 
ST | 00 11 01 00 | 642
LD | 00 10 10 00 | 
LD | 00 01 11 00 | 
ST | 00 10 01 00 | 124
LD | 00 10 00 00 | 
LD | 00 10 10 00 | 
Address (binary) | Data (dec)
00 00 10 00 | 435
00 00 11 00 | 9
00 01 00 00 | 47
00 01 01 00 | 13
00 01 10 00 | 7586
00 01 11 00 | 86
00 10 00 00 | 43
00 10 01 00 | 124
00 10 10 00 | 673
00 10 11 00 | 4
00 11 00 00 | 972
00 11 01 00 | 642
Sets | Tag | V bit | Data
00 | 0001 | 1 | 47
01 |  | 0 | 
10 | 0010 | 1 | 673
11 | 0001 | 1 | 86
Cache Miss = 6 Cache Hit = 2

## Slide 23: Example 02
Op | Address(binary) | Data (dec)
LD | 00 01 11 00 | 
LD | 00 10 10 00 | 
ST | 00 10 01 00 | 32
LD | 00 01 00 00 | 
ST | 00 11 01 00 | 642
LD | 00 10 10 00 | 
LD | 00 01 11 00 | 
ST | 00 10 01 00 | 124
LD | 00 10 00 00 | 
LD | 00 10 10 00 | 
Address (binary) | Data (dec)
00 00 10 00 | 435
00 00 11 00 | 9
00 01 00 00 | 47
00 01 01 00 | 13
00 01 10 00 | 7586
00 01 11 00 | 86
00 10 00 00 | 43
00 10 01 00 | 124
00 10 10 00 | 673
00 10 11 00 | 4
00 11 00 00 | 972
00 11 01 00 | 642
Sets | Tag | V bit | Data
00 | 0010 | 1 | 43
01 |  | 0 | 
10 | 0010 | 1 | 673
11 | 0001 | 1 | 86
Cache Miss = 7 Cache Hit = 2

## Slide 24: Example 02
Op | Address(binary) | Data (dec)
LD | 00 01 11 00 | 
LD | 00 10 10 00 | 
ST | 00 10 01 00 | 32
LD | 00 01 00 00 | 
ST | 00 11 01 00 | 642
LD | 00 10 10 00 | 
LD | 00 01 11 00 | 
ST | 00 10 01 00 | 124
LD | 00 10 00 00 | 
LD | 00 10 10 00 | 
Address (binary) | Data (dec)
00 00 10 00 | 435
00 00 11 00 | 9
00 01 00 00 | 47
00 01 01 00 | 13
00 01 10 00 | 7586
00 01 11 00 | 86
00 10 00 00 | 43
00 10 01 00 | 124
00 10 10 00 | 673
00 10 11 00 | 4
00 11 00 00 | 972
00 11 01 00 | 642
Sets | Tag | V bit | Data
00 | 0010 | 1 | 43
01 |  | 0 | 
10 | 0010 | 1 | 673
11 | 0001 | 1 | 86
Cache Miss = 7 Cache Hit = 3

## Slide 25: Example 03
Consider a 4-way associative cache with block size 2 bytes and total capacity of 16bytes. The tag bits are 3 bits long.
What are the total address bits?

## Slide 26: Example 03
Op | Address(dec)
LD | 24
LD | 25
LD | 26
LD | 24
LD | 21
LD | 26
LD | 24
LD | 30
LD | 27
Address (dec) | Data (dec)
20 | 7
21 | 3
22 | 27
23 | 32
24 | 101
25 | 78
26 | 59
27 | 24
28 | 56
29 | 87
30 | 36
31 | 98
Set | Tag | LRU bit | V bit | Data | 
 |  |  |  | 0 | 1
0 | 110 | 10 | 0 | 101 | 78
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
1 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
Cache Miss = 0 Cache Hit = 0

## Slide 27: Example 03
Op | Address(dec)
LD | 24
LD | 25
LD | 26
LD | 24
LD | 21
LD | 26
LD | 24
LD | 30
LD | 27
Address (dec) | Data (dec)
20 | 7
21 | 3
22 | 27
23 | 32
24 | 101
25 | 78
26 | 59
27 | 24
28 | 56
29 | 87
30 | 36
31 | 98
Set | Tag | LRU bit | V bit | Data | 
 |  |  |  | 0 | 1
0 | 110 | 10 | 0 | 101 | 78
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
1 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
Cache Miss = 0 Cache Hit = 0
Convert to
binary
24
11000
Tag Bits Set bits Offset bits

## Slide 28: Example 03
Op | Address(dec)
LD | 24
LD | 25
LD | 26
LD | 24
LD | 21
LD | 26
LD | 24
LD | 30
LD | 27
Address (dec) | Data (dec)
20 | 7
21 | 3
22 | 27
23 | 32
24 | 101
25 | 78
26 | 59
27 | 24
28 | 56
29 | 87
30 | 36
31 | 98
Cache Miss = 1 Cache Hit = 0
Convert to
binary
24
11000
Tag Bits Set bits Offset bits
Set | Tag | LRU bit | V bit | Data | 
 |  |  |  | 0 | 1
0 | 110 | 00 | 1 | 101 | 78
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
1 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 

## Slide 29: Example 03
Op | Address(dec)
LD | 24
LD | 25
LD | 26
LD | 24
LD | 21
LD | 26
LD | 24
LD | 30
LD | 27
Address (dec) | Data (dec)
20 | 7
21 | 3
22 | 27
23 | 32
24 | 101
25 | 78
26 | 59
27 | 24
28 | 56
29 | 87
30 | 36
31 | 98
Cache Miss = 1 Cache Hit = 1
Convert to
binary
25
11000
Tag Bits Set bits Offset bits
Set | Tag | LRU bit | V bit | Data | 
 |  |  |  | 0 | 1
0 | 110 | 00 | 1 | 101 | 78
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
1 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 

## Slide 30: Example 03
Op | Address(dec)
LD | 24
LD | 25
LD | 26
LD | 24
LD | 21
LD | 26
LD | 24
LD | 30
LD | 27
Address (dec) | Data (dec)
20 | 7
21 | 3
22 | 27
23 | 32
24 | 101
25 | 78
26 | 59
27 | 24
28 | 56
29 | 87
30 | 36
31 | 98
Cache Miss = 2 Cache Hit = 1
Convert to
binary
26
11010
Tag Bits Set bits Offset bits
Set | Tag | LRU bit | V bit | Data | 
 |  |  |  | 0 | 1
0 | 110 | 00 | 0 | 101 | 78
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
1 | 110 | 00 | 1 | 59 | 24
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 

## Slide 31: Example 03
Op | Address(dec)
LD | 24
LD | 25
LD | 26
LD | 24
LD | 21
LD | 26
LD | 24
LD | 30
LD | 27
Address (dec) | Data (dec)
20 | 7
21 | 3
22 | 27
23 | 32
24 | 101
25 | 78
26 | 59
27 | 24
28 | 56
29 | 87
30 | 36
31 | 98
Cache Miss = 2 Cache Hit = 2
Set | Tag | LRU bit | V bit | Data | 
 |  |  |  | 0 | 1
0 | 110 | 00 | 1 | 101 | 78
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
1 | 110 | 00 | 1 | 59 | 24
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
24
11000
Tag Bits Set bits Offset bits

## Slide 32: Example 03
Op | Address(dec)
LD | 24
LD | 25
LD | 26
LD | 24
LD | 21
LD | 26
LD | 24
LD | 30
LD | 27
Address (dec) | Data (dec)
20 | 7
21 | 3
22 | 27
23 | 32
24 | 101
25 | 78
26 | 59
27 | 24
28 | 56
29 | 87
30 | 36
31 | 98
Cache Miss = 3 Cache Hit = 2
Set | Tag | LRU bit | V bit | Data | 
 |  |  |  | 0 | 1
0 | 110 | 01 | 1 | 101 | 78
 | 101 | 00 | 1 | 7 | 3
 |  |  | 0 |  | 
 |  |  | 0 |  | 
1 | 110 | 00 | 1 | 59 | 24
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
21
10101
Tag Bits Set bits Offset bits

## Slide 33: Example 03
Op | Address(dec)
LD | 24
LD | 25
LD | 26
LD | 24
LD | 21
LD | 26
LD | 24
LD | 30
LD | 27
Address (dec) | Data (dec)
20 | 7
21 | 3
22 | 27
23 | 32
24 | 101
25 | 78
26 | 59
27 | 24
28 | 56
29 | 87
30 | 36
31 | 98
Cache Miss = 3 Cache Hit = 3
Set | Tag | LRU bit | V bit | Data | 
 |  |  |  | 0 | 1
0 | 110 | 01 | 1 | 101 | 78
 | 101 | 00 | 1 | 7 | 3
 |  |  | 0 |  | 
 |  |  | 0 |  | 
1 | 110 | 00 | 1 | 59 | 24
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
Convert to
binary
26
11010
Tag Bits Set bits Offset bits

## Slide 34: Example 03
Op | Address(dec)
LD | 24
LD | 25
LD | 26
LD | 24
LD | 21
LD | 26
LD | 24
LD | 30
LD | 27
Address (dec) | Data (dec)
20 | 7
21 | 3
22 | 27
23 | 32
24 | 101
25 | 78
26 | 59
27 | 24
28 | 56
29 | 87
30 | 36
31 | 98
Cache Miss = 3 Cache Hit = 4
Set | Tag | LRU bit | V bit | Data | 
 |  |  |  | 0 | 1
0 | 110 | 00 | 1 | 101 | 78
 | 101 | 01 | 1 | 7 | 3
 |  |  | 0 |  | 
 |  |  | 0 |  | 
1 | 110 | 00 | 1 | 59 | 24
 |  |  | 0 |  | 
 |  |  | 0 |  | 
 |  |  | 0 |  | 
24
11000
Tag Bits Set bits Offset bits

## Slide 35: Example 03
Op | Address(dec)
LD | 24
LD | 25
LD | 26
LD | 24
LD | 21
LD | 26
LD | 24
LD | 30
LD | 27
Address (dec) | Data (dec)
20 | 7
21 | 3
22 | 27
23 | 32
24 | 101
25 | 78
26 | 59
27 | 24
28 | 56
29 | 87
30 | 36
31 | 98
Cache Miss = 4 Cache Hit = 4
Set | Tag | LRU bit | V bit | Data | 
 |  |  |  | 0 | 1
0 | 110 | 01 | 1 | 101 | 78
 | 101 | 00 | 1 | 7 | 3
 |  |  | 0 |  | 
 |  |  | 0 |  | 
1 | 110 | 01 | 1 | 59 | 24
 | 111 | 00 | 1 | 36 | 98
 |  |  | 0 |  | 
 |  |  | 0 |  | 
30
11110
Tag Bits Set bits Offset bits

## Slide 36: Example 03
Op | Address(dec)
LD | 24
LD | 25
LD | 26
LD | 24
LD | 21
LD | 26
LD | 24
LD | 30
LD | 27
Address (dec) | Data (dec)
20 | 7
21 | 3
22 | 27
23 | 32
24 | 101
25 | 78
26 | 59
27 | 24
28 | 56
29 | 87
30 | 36
31 | 98
Cache Miss = 4 Cache Hit = 5
Set | Tag | LRU bit | V bit | Data | 
 |  |  |  | 0 | 1
0 | 110 | 01 | 1 | 101 | 78
 | 101 | 00 | 1 | 7 | 3
 |  |  | 0 |  | 
 |  |  | 0 |  | 
1 | 110 | 00 | 1 | 59 | 24
 | 111 | 01 | 1 | 36 | 98
 |  |  | 0 |  | 
 |  |  | 0 |  | 
27
11011
Tag Bits Set bits Offset bits